## Slide 1: COP 6611: Operating Systems Project 1
Instructor: Xinming (Simon) Ou
TAs: Anwesh Tuladhar
Jaleel Ahmed
Guojun (Luis) Liu
Acknowledgement: some slides are taken from CS422/522 lectures taught by Professor Zhong Shao at Yale University.

## Slide 2: Project 0: What was accomplished ? (1)
Boot0 from 0x7c00 to 0x7e00 => 446 bytes + 66 bytes partition table
Boot1 from 0x7e00 to 0xfa00 => 62 sectors (512 bytes * 62 = 31KB)
Enabled 32-bit Protected Mode.
parse_e820():
  Parse the memory map loaded in boot1.S using BIOS function INT 0x15.
  Now stored in mboot_info.
load_kernel()
  Loads the first 8 sectors of the hard disk’s bootable partition to virtual address 0x20000.
  Check if it is a valid ELF (Magic number = 0x7F followed by ELF in ASCII. = 0x7f454c46).
  Load each program segment at the corresponding virtual addresses.
  Find the entry point from elf header.
Notes: We only have 1 partition.
kernel is loaded to 0x100000 (= 1MB mark) which is right after the BIOS.

## Slide 3: Project 0: What was accomplished ? (2)
exec_kernel()
  Store a magic number into %eax
  Store pointer to mboot_info in %ebx.
  Jump to entry.
entry.S
  Prints “Successfully loaded the Kernel ...”

## Slide 4: Project 1
entry.S: Updated
  Check if kernel was loaded successfully.
  Clear EFLAGS register.
  Allocated memory for kernel stack and setup %ebp and %esp.
  Call kern_init(mboot_info).
init.c
  Functions defined: kern_init() and kern_main().
  The goal of this assignment is to make this kernel execute.
  Specifically, you will be implementing a 2-level paging mechanism for a 4GB address space.

## Slide 5: Address Translation in x86
Segmentation
Mechanism
Selector
Virtual Address
Offset
Software
Paging
Mechanism
Linear Address
Physical Address
RAM
A virtual address consists of a segment selector and an offset within the segment.
  A C pointer is the "offset" component of the virtual address.
A linear address is what you get after segment translation but before page translation.
A physical address is what you finally get after both segment and page translation. It goes out on the hardware bus to your RAM.
We installed a Global Descriptor Table (GDT) that effectively disabled segment translation by setting all segment base addresses to 0 and limits to 0xffffffff. Hence the "selector" has no effect and the linear address always equals the offset of the virtual address.
Therefore, we can focus solely on page translation.
Notes: A C pointer is the "offset" component of the virtual address. In mCertiKOS, we installed a Global Descriptor Table (GDT) that effectively disabled segment translation by setting all segment base addresses to 0 and limits to 0xffffffff. Hence the "selector" has no effect and the linear address always equals the offset of the virtual address.

## Slide 6: High level view
To implement a two-level paging scheme for a 4GB address space, we will need to accomplish the following tasks:
Setup the page table in memory.
  Implement low level physical memory access mechanism.
  Implement 2-level paging address translation mechanism.
Point the hardware to the location of the page table.
Enable paging.

## Slide 7: Code Overview
Execution modes:
  Normal: make
  Test: make TEST=1
  Solutions: make SOL=1, make TEST=1 SOL=1
Folder structure
Physical Memory Management (pmm)
Virtual Memory Management (vmm)

## Slide 8: The Layered Design
Bootloader
MATIntro
MATInit
MATOp
MATContainer
MPTIntro
MPTOp
MPTComm
MPTKern
Physical Memory Management
(PMM)
Virtual Memory Management
(VMM)
Data Structure: Allocation Table (AT)
Initial Physical memory using AT
Export Operations on physical memory: palloc, free
Data Structure: SContainer -> Track per process memory usage.
Data Structures: PDirPool (+PTbl), IDPTbl
Vaddr based access to MPTIntro
Common operations: allocate and free page table
MPTNew
Map and unmap page tables to processes
API to allocate new pages for process on page fault

## Slide 9: Physical Memory Management (PMM)
To set up the page table in memory:
Track the available physical memory.
Not all of memory can be used.
  Which page is reserved?
  Which page is used by the kernel?
  Which page is used by the user?
Which pages are allocated? Which pages are free to use?
How to allocate a new page? How to deallocate a used page?

## Slide 10: PMM: Data structures
ATStruct:
  MATIntro layer.
  Data structure used to track the physical memory at page granularity.
  Each page in physical memory will have a corresponding ATStruct associated with it.
  It tracks the permission and allocation status for that page.
ATStruct | 
perm | allocated

## Slide 11: PMM: Representing the entire physical memory
ATStruct = 1 page
Array of ATStruct = Entire memory
  Size of each page = 4KB
  Max. number of pages = 4GB/4KB = 2^20 pages ( AT[1<<20] = AT[1048576])
MATIntro layer: Deals with manipulating and interacting with this data structure.
Address | Index into AT (# page) | ATStruct | 
0x0 | 0 | perm | allocated
0x1000 | 1 | perm | allocated

## Slide 12: PMM: Initializing AT
Permissions:
  perm = 0: Reserved by the BIOS
  perm = 1: Kernel memory
  perm > 1: Normal (available for user)
Each virtual address space will reflect this structure as well.
0x00000000
Kernel
VM_USERLO (0x40000000)
Available for use
User
0xFFFFFFFF (4GB)
Reserved for Kernel
VM_USERHI (0xF0000000)
Kernel
Reserved for Kernel
Physical Memory/AT

## Slide 13: PMM: Tracking resource usage for each process
Identifying each process:
  A process is assigned a unique ID (PID) when it is spawned.
SContainer:
  MContainer layer
  Data structure used to track:
    quota: Maximum memory quota of the process
    usage: The current memory usage of the process
    parent: The PID of the parent
    nchildren: The number of child processes
    used: Whether the current container is used by a process.
  Soundness: The sum of the available quotas (i.e., quota minus usage) of all used IDs is at most the number of pages available for allocation.
MContainer layer: Deals with manipulating and interacting with this data structure.

## Slide 14: Virtual Memory Management (VMM)
Each process will have it’s own 4GB virtual address space.
The virtual address will be translated using two level paging scheme.
We will maintain one page structure for each process.
    Switch page structures when we switch among different processes.
We will statically allocate page directories, and maintain the second level page tables dynamically.
Remember that each page is 4KB.
Size of each page table entry (pte) = 4 bytes.
Number of pte’s per page = 4KB/4byes = 1024
Page Table Entry (PTE)
31 12 | 11 3 | 2 | 1 | 0
Page frame address 31..12 | Flags | U/S | R/W | P

## Slide 15: VMM: Tracking page structure per process
PDirPool:
  MPTIntro layer
  This is a 2-dimensional array where we statically allocate page directories for each process. (1st dimension = PID, 2nd dimension = Page directory)
  We will have 1024 page directory entries for each process. The page table entries within each page directory will be allocated dynamically.

## Slide 16: VMM: PDirPool
0 | Page directory entry 0
1 | Page directory entry 1
… | 
1023 | Page directory entry 1023
Index
Process 0
0 | Page directory entry 0
1 | Page directory entry 1
… | 
1023 | Page directory entry 1023
Process 1
0 | Page directory entry 0
1 | Page directory entry 1
… | 
1023 | Page directory entry 1023
Process 2
0 | Page table entry 0
1 | Page table entry 1
… | 
1023 | Page table entry 1023
0 | Page table entry 0
1 | Page table entry 1
… | 
1023 | Page table entry 1023
0 | Page table entry 0
1 | Page table entry 1
… | 
1023 | Page table entry 1023
Index

## Slide 17: VMM: Identity Page Table
Kernel needs to access the physical memory directly.
  But once in protected mode and paging is turned on, there is no way to directly use the physical addresses as virtual memory translation cannot be by-passed.
Solution:
  We will reserve the page structure with index 0 for the kernel (process 0).
  We will use Identity page table mapping (virtual address is same as physical address) for the entire page structure 0.
  The kernel portion of each page structure will also have identity mapping.
IDPTbl:
  Instead of repeatedly allocating the same identity second level page tables, we statically allocate one and point every appropriate page directory index to the same page table entry.
  Permissions for the kernel region (< VM_USERLO and >= VM_USERHI) should set the present bit, writeable bit and global bit in the identity map.
Notes: - If the G-bit is set, then the entry is global to all processes and they can all access the physical page it maps, subject to other access rights.

## Slide 18: DEMO